U.S. Department of Housing and Urban Development

Office of Public Housing

UFAS On-Site Review Checklist

This checklist was developed locally to provide the reviewer with a general guide for reviewing a Public Housing Site for compliance with the Uniform Federal Accessibility Standards (UFAS).  This checklist is meant to provide an overview of the accessible features for both units and nondwelling spaces and does not include every item from the UFAS.  The reviewer should take both the UFAS and a tape measure to the site to determine compliance.  The first four pages of this checklist provides for the review of non-dwelling space.  Separate dwelling unit sheets should be provided for each unit inspected.

| Housing Authority Name: | Number of Units: |
| --- | --- |
| Project Name/Number: | Family/Elderly: |
| List Units Inspected: |

| General Development Information | Yes | No | N/A | Notes |
| --- | --- | --- | --- | --- |
| Does this development have accessible units? |  |  |  |  |
| If yes, how many? Physical #___%___ Vision/Impaired #___%___ |  |  |  |  |
| If not, has this project undergone any modernization since 1992. If yes, what components have been replace? |  |  |  |  |
| Did the PHA meet the requirements of Part 8, Other Alterations when conducting modernization activities? |  |  |  |  |
| Site | Yes | No | N/A | Notes |
| Accessible Routes: Determine if there is an accessible route to and from all common areas? (UFAS 4.3) |  |  |  |  |
| Are the accessible pathways free of steps and stairs? (UFAS 4.3.8) |  |  |  |  |
| Are the accessible pathways at least 36 inches wide? (UFAS 4.3.3) |  |  |  |  |
| If the pathways are less than 60 inches wide, are there passing spaces at least 60 inches wide and 60 inches long at reasonable intervals not exceeding 200 feet? (UFAS 4.3.4) |  |  |  |  |
| Are accessible pathway surfaces stable, firm and slip-resistant? (UFAS 4.5.1) |  |  |  |  |
| Is the smaller dimension of grating openings no more than 1/2 inch, and are long dimensions of rectangular spaces placed perpendicular to the usual direction of travel? (UFAS 4.5.4) |  |  |  |  |
| Is the slope of the accessible pathway no greater than 1:20 and the cross slope no greater than 1:50? (UFAS 4.3.7) |  |  |  |  |
| If there is a change in level >1/2 inch anywhere on the accessible route? (UFAS 4.3.8) |  |  |  |  |
| Parking | Yes | No | N/A | Notes |
| Are the required number of accessible parking spaces provided? (UFAS 4.1.1(5a) |  |  |  |  |
| Are accessible parking spaces the closest spaces to the building’s accessible entrance? (UFAS 4.6.2) |  |  |  |  |
| Are accessible parking spaces at least 96 inches wide with a demarcated adjacent access aisle of 60 inches? (UFAS 4.6.3) (Note that two spaces may share a common aisle.) |  |  |  |  |
| Does the access aisle connect directly to the accessible route? If the parking space is designated as a van space, is the adjacent aisle at least 96 inches wide? (UFAS 4.6.3) |  |  |  |  |
| Are the spaces and aisles level with no slope greater than 1:50? (This means a curb ramp cannot project into the access aisle.) (UFAS 4.6.3) |  |  |  |  |
| Does each accessible parking space have a vertical sign that is unobscured by a parked vehicle and shows the universal symbol of accessibility? (UFAS 4.6.4) |  |  |  |  |
| Passenger Loading Zone | Yes | No | N/A | Notes |
| If a passenger loading zone is provided is it accessible? (UFAS 4.6.5) |  |  |  |  |
| Is there a sign displaying the international symbol of accessibility at the passenger loading zone? (UFAS 4.1.1(7)) |  |  |  |  |
| Is there a 5’ by 20’ pedestrian aisle parallel to the vehicle pull-up space? (UFAS 4.6.5) |  |  |  |  |
| Is the pedestrian aisle and pull-up space level, with no slope greater than 1:50? (UFAS 4.6.5) |  |  |  |  |
| Is the pedestrian aisle and parking surface stable, firm, and slip-resistant? (UFAS 4.5.1) |  |  |  |  |
| Is there at least 114 inches of vertical clearance at the passenger loading zone? (UFAS 4.6.6) |  |  |  |  |
| RAMPS | Yes | No | N/A | Notes |
| Are ramp slopes 1:12 or less? (UFAS 4.8.2) |  |  |  |  |
| Is the rise for any run 30 inches or less? |  |  |  |  |
| Is the cross slope of the ramp surface no greater than 1:50? (UFAS 4.8.6) |  |  |  |  |
| Is the ramp surface non-slip? (UFAS 4.5) |  |  |  |  |
| Is the clear width of the ramp 36 inches or more? (UFAS 4.8.3) |  |  |  |  |
| Is there a level landing at the top and bottom of each run? (UFAS 4.8.4) |  |  |  |  |
| Is each landing at least as wide as the ramp and 60 inches long? (UFAS 4.8.4(2) |  |  |  |  |
| Where the ramp changes direction, is the landing at least 60 by 60 inches? (UFAS 4.8.4(4)) |  |  |  |  |
| If the ramp rises more than 6 inches or is longer than 72 inches, does it have a handrail on each side? (UFAS 4.8.5) |  |  |  |  |
| On dogleg or switchback ramps, is the inside handrail continuous? (UFAS 4.8.5(1)) |  |  |  |  |
| Is the gripping surface continuous? (4.8.5(4) |  |  |  |  |
| Is the top of the handrail between 30 and 34 inches above the ramp surface? (UFAS 4.8.5(5)) |  |  |  |  |
| At ends of handrails, is there at least 12 inches of level handrail beyond the top and bottom of the ramp segment? (UFAS 4.8.5(2) |  |  |  |  |
| Are the ends of handrails rounded or returned smoothly to the floor, wall, or post? (4.8.5(6)) |  |  |  |  |
| Is the diameter of the handrail between 1-1/4 inches and 1-1/2 inches? (UFAS 4.8.5; 4.26) |  |  |  |  |
| If a ramp or landing has a drop off, does it have a 2 inch curb, a wall, railings or projecting surfaces which prevent people from falling off? (UFAS 4.8.7) |  |  |  |  |
| Are ramps designed so that water will not accumulate on walking surfaces? (UFAS 4.8.8) |  |  |  |  |
| STAIRS | Yes | No | N/A | Notes |
| In any one flight do all the steps have uniform riser height and tread width? Are the risers closed? (UFAS 4.9.2) |  |  |  |  |
| Are the treads a minimum of 11 inches measured from nosing to nosing? (UFAS 4.9.2) |  |  |  |  |
| Do the nosings project no more than 1-1/2 inches? (UFAS 4.9.3) |  |  |  |  |
| Do stairways have continuous handrails at both sides of all steps? (UFAS 4.9.4) |  |  |  |  |
| On dogleg or switchback stairs, is the inside handrail continuous? (UFAS 4.9.4(1)) |  |  |  |  |
| At ends of handrails, is there at least 12 inches of level handrail beyond the top riser? (4.9.4(2)) |  |  |  |  |
| Are the tops of handrails between 30 and 34 inches above the nosings? (UFAS 4.9.4(5)) |  |  |  |  |
| Is the diameter of the handrail between1-1/4 inches and 1-1/2 inches (UFAS 4.9.4; 4.26) or Does the shape provide an equivalent gripping surface? |  |  |  |  |
| Building: | Yes | No | N/A | Notes |
| Entrance – Is there at least one principal entrance at each on-grade floor level in compliance? (UFAS 4.1.2(8)) |  |  |  |  |
| Building Accessible Route: Is there at least one accessible route complying with 4.3 to connect accessible building or facility entrances with all accessible spaces within the building or facility? (UFAS 4.1.2(1)) |  |  |  |  |
| When a door is open 90 degrees, is there a clear opening at least 32 inches measured between the face of the door and the door stop on the latch side? (UFAS 4.13.5) |  |  |  |  |
| Are door approaches adequate per Figure 25. |  |  |  |  |
| If there are two doors in series, is the clear space between the walls at either end of the vestibule at least 48 inches plus the width of the door?(UFAS 4.13.7) |  |  |  |  |
| Are all handles, locks, and latches operable with one hand? Are they operable without tight pinching, tight grasping or twisting of the wrist? (UFAS 4.13.9) |  |  |  |  |
| Building Lobbies and Corridors | Yes | No | N/A | Notes |
| If more than one means of egress is required by the fire code, is more than one accessible? (UFAS 4.3.10; 4.1.2(7d)) |  |  |  |  |
| Is there a 36” accessible route connecting the accessible entrance with all elements, spaces and dwelling units w/I the building? (UFAS 4.3.2(3)) |  |  |  |  |
| Are doorways at least 32 inches in clear opening width? (UFAS 4.13.5) |  |  |  |  |
| Are the floors in all accessible areas and routes stable, firm, and slip-resistant? (UFAS 4.5.1) |  |  |  |  |
| Elevators: | Yes | No | N/A | Notes |
| Are the hallway call buttons centered at 42 inches above the Floor? (UFAS 4.10.3) |  |  |  |  |
| Do they have visual signals to indicate when each call is registered and answered? |  |  |  |  |
| Is the button designating the up direction above the down button? |  |  |  |  |
| Do audible signals sound once for up and twice for down, or do they have verbal annunciators that say “up” or “down”? |  |  |  |  |
| Does the floor area of the car allow maneuvering room for wheelchair users to enter the car, reach the controls, and exit? (Figure 22) |  |  |  |  |
| Accessible Public Bathrooms | Yes | No | N/A | Notes |
| Are the toilet rooms located on an accessible Route? (UFAS 4.22.1) |  |  |  |  |
| Is there an unobstructed turning space (a 60 inch diameter circle or T-shaped space) in the toilet room? (UFAS 4.22.3) |  |  |  |  |
| Does no door swing into a required clear floor space at an accessible fixture? (UFAS 4.22.2) |  |  |  |  |
| Do toilet stalls meet the requirements of Figure 30a? (Arrangements may be reversed. Alternate stalls are not permitted in new construction.) |  |  |  |  |
| Do nonpartitioned toilets spaces meet the requirements of Figure 28. |  |  |  |  |
| Do nonpartitioned grab bars and water closets meet the requirements of Figure 29? |  |  |  |  |
| Are flush controls automatic or operable with one hand? Are they mounted on the wide side of the toilet area? (UFAS 4.16.5) |  |  |  |  |
| If urinals are provided, does at least one meet the requirements? (UFAS 4.18) |  |  |  |  |
| Does the lavatory meet the requirements of Figure 31 and 32? |  |  |  |  |
| Are hot water pipes and drain pipes insulated or otherwise covered? (UFAS 4.19.4) |  |  |  |  |
| Can the faucet be operated with one hand without tight grasping, pinching, or twisting of the wrist? (UFAS 4.19.5) |  |  |  |  |
| Laundry Spaces | Yes | No | N/A | Notes |
| Is at least one washing machines and clothes dryer front loading? (UFAS 4.34.7.2) |  |  |  |  |
| Is adequate clear floor space provided? (UFAS 4.27.2) |  |  |  |  |

Dwelling Unit Review

The reviewer should use a separate copy of this portion of the checklist for each unit reviewed

Project Number: ____________	Dwelling Unit Number: ____________	# Bedrooms: ____________

| Dwelling Unit Reviews | Yes | No | N/A | Notes |
| --- | --- | --- | --- | --- |
| Are the accessible dwelling units designed for permanent accessibility or adaptability? |  |  |  |  |
| If they are designed for adaptability, is consumer information provided in each adaptable dwelling unit available for occupancy? (UFAS 4.34.4) |  |  |  |  |
| Site | Yes | No | N/A | Notes |
| If parking is provided for all residents, is one accessible parking space provided for each accessible dwelling unit? (UFAS 4.1.1(d)) |  |  |  |  |
| Review the parking section of this form to determine compliance with requirements for units. Is the parking in compliance? |  |  |  |  |
| Are mailbox areas accessible? (UFAS 4.2) |  |  |  |  |
| Is there access to all areas intended for resident use (clothes lines, patios, decks, etc..)? |  |  |  |  |
| RAMPS | Yes | No | N/A | Notes |
| Are ramp slopes 1:12 or less? (UFAS 4.8.2) |  |  |  |  |
| Is the rise for any run 30 inches or less? |  |  |  |  |
| Is the cross slope of the ramp surface no greater than 1:50? (UFAS 4.8.6) |  |  |  |  |
| Is the ramp surface non-slip? (UFAS 4.8.6; 4.5) |  |  |  |  |
| Is the clear width of the ramp 36 inches or more? (UFAS 4.8.3) |  |  |  |  |
| Is there a level landing at the top and bottom of each run? (UFAS 4.8.4) |  |  |  |  |
| Is each landing at least as wide as the ramp and 60 inches long? |  |  |  |  |
| Where the ramp changes direction, is the landing at least 60 by 60 inches? |  |  |  |  |
| If the ramp rises more than 6 inches or is longer than 72 inches, does it have a handrail on each side? (UFAS 4.8.5) |  |  |  |  |
| On dogleg or switchback ramps, is the inside handrail continuous? |  |  |  |  |
| Is the gripping surface continuous? |  |  |  |  |
| Is the top of the handrail between 30 and 34 inches above the ramp surface? |  |  |  |  |
| At ends of handrails, is there at least 12 inches of level handrail beyond the top and bottom of the ramp segment? |  |  |  |  |
| Are the ends of handrails rounded or returned smoothly to the floor, wall, or post? |  |  |  |  |
| Is the diameter of the handrail between 1-1/4 inches and 1-1/2 inches? (UFAS 4.8.5; 4.26) |  |  |  |  |
| If a ramp or landing has a drop off, does it have a 2 inch curb, a wall, railings or projecting surfaces which prevent people from falling off? (UFAS 4.8.7) |  |  |  |  |
| Are ramps designed so that water will not accumulate on walking surfaces? (UFAS 4.8.8) |  |  |  |  |
| Doors | Yes | No | N/A | Notes |
| Do all doors have adequate approaches in accordance with Figure 25? |  |  |  |  |
| Are door widths adequate? (UFAS 4.13.1) Are doors easy to open and close? |  |  |  |  |
| Is the door threshold >3/4”? (UFAS 4.13.8) |  |  |  |  |
| Do all door have lever type latches? |  |  |  |  |
| Are door peep holes at a reasonable height? |  |  |  |  |
| Kitchen Note that adaptable kitchens may have removable components that will provide these features | Yes | No | N/A | Notes |
| Is the clearance between all opposing cabinet, counter, appliances or walls at least 40 inches except in U-shaped kitchens where the clearance must be 60 inches? (UFAS 4.34.6.1) |  |  |  |  |
| Is the bottom edge of overhead cabinets located no more than 48” above the floor in accordance with UFAS Figure 5. |  |  |  |  |
| Is there 30 x 48 inches clear space at appliances? (UFAS 4.34.6.2) |  |  |  |  |
| Is there at least one 30 inch open work surface which is no more than 34 inches above the floor measured from the floor to the top of the counter? (UFAS 4.34.6.4) |  |  |  |  |
| Is the area beneath the sink accessible by wheelchair and is there a 30 x 48 inches clear floor space allowing a forward approach to the sink? (UFAS 4.34.6.5(7)) |  |  |  |  |
| Are the hot water and drain pipes insulated or otherwise covered? |  |  |  |  |
| Is a clear floor space at least 30 x 48 inches which allow either a forward or a parallel approach provided at the range, oven or cooktop? (UFAS 4.34.6.6;4.34.6.2) |  |  |  |  |
| Does the location of the controls allow them to be used without reaching across burners? |  |  |  |  |
| If the oven is the side opening type, is the door latch next to the open counter space and is there a pull out shelf under the oven at least as wide as the oven and 10 inches deep? |  |  |  |  |
| If the refrigerator/freezer is an over/under type, is at least 50% of the freezer space within 54 inches of the floor and if 100% of freezer space is not within these limits, is the freezer self-defrosting? (UFAS 4.34.6.8) |  |  |  |  |
| Bathrooms | Yes | No | N/A | Notes |
| Is at least one full bathroom accessible or adaptable, including a water closet, a lavatory and a bathtub or shower? (UFAS 4.34.2) |  |  |  |  |
| Is there an unobstructed turning space (a 60 inch diameter circle or T-shaped space) in the toilet room? (UFAS 4.22.3) |  |  |  |  |
| Do water closet spaces meet the requirements of Figure 28 and 29. Is the seat between 17” and 19”? |  |  |  |  |
| Do bathtub spaces meet the requirements of Figure 33 and 34? Is a seat provided? Is a handheld hoze provided? |  |  |  |  |
| If showers provided, does it meet the requirements of Figures 35, 36 and 37? |  |  |  |  |
| Are grab bars installed securely in the locations shown and do they meet the standards? (UFAS 4.16.4) |  |  |  |  |
| Do lavatory spaces meet the requirements of Figure 31 and 32? |  |  |  |  |
| Are all fixtures lever type? (UFAS 4.27.4) |  |  |  |  |
| Is all piping covered or insulated to prevent injury? (UFAS 4.19.4) |  |  |  |  |
| If a medicine cabinet is provided, is there a usable shelf inside no higher than 44 inches above the floor? (UFAS 4.34.5.3(3)) |  |  |  |  |
| Other Items | Yes | No | N/A | Notes |
| Is closet shelving at no more than 48” |  |  |  |  |
| Vision and Hearing | Yes | No | N/A | Notes |
| Are vision and hearing units provided in the percentage required? |  |  |  |  |
| Are vision and hearing units separate from physically accessible units? |  |  |  |  |
| Is there a visual alarm connected to the building emergency alarm system? Or, is there a standard 110-volt electrical receptacle into which a visual alarm could be connected? (UFAS 4.34.1) |  |  |  |  |

Other Issues:

Sketch or place pictures of any notable items in this space: